## Slide 1: EP1000
Actuators Assignment

## Slide 2: Actuators
A component of a machine that moves/controls a mechanism in a system.
An “output” device.
Examples:
  Displays – LED, LCD, Neopixels
  Motors – DC Motors, Stepper Motors, Servo Motors
  Valves – Water, gas
  Solenoids – controls heavier voltages, currents
  Sounds – buzzers, alarms

## Slide 3: Display devices
The most common output display devices used in projcects are:
  LEDs (indicators)
  LCD (display panels, information) 16x2, 20x2
  NeoPixels (strip lights, multi RGB leds)
  7-segment tube displays
  Dot-matrix displays (running messages)
  Oled displays

## Slide 4: LEDs
Types: single, RGB, 7-segment
Identify the Anode (or Cathode)
Ensure there is proper current limiting resistors
You need a delay to maintain the display (persistence of vision)
You can use PWM to obtain different intensity levels.
Uno Random RGB Led using PWM

## Slide 5: LCD Displays
Common method of displaying information
Usually Hitachi HD44780 control (8 data, RS, RW, En)
Made simpler using an I2C 1602 controller for the LCD panel
Library: LiquidCrystal I2C by Frank de Brabander.
Reference: LastMinuteEngineers

## Slide 6: I2C Interface
A method of Serial communication.
Uses 2 wires (SDA, SCL) to communicate between devices.
Each device has a unique address which identifies it.
Can have up to 1024 devices
Ref: How To Mechantronics How I2C Communication Works and How to use it with Arduino

## Slide 7: Identifying I2c devices
Use the controller (master) to scan the bus for devices (slaves).
The addresses will be printed out on the Serial Monitor.
You can then use the address to write/read from the device.
Library: Arduino Wire Library
Example code is usually provided by the device library.

## Slide 8: Writing to I2C LCD display
Using the LiquidCrystal_I2C library.
Create the object lcd
Initial housekeeping
  Initialise
  Clear the screen
  Turn on backlight
To print messages
  Position the cursor
  Print the message

## Slide 9: Tube 7-Segment

## Slide 10: EP1000
Actuators
End