## Slide 1: EP1000
Computer Controlled Cutting 2

## Slide 2: Lasercut Parametric Box
Boxes are useful in all projects as they provide housing or containment.
Making the box parametric allows changes, accommodating for boxes of different sizes, types.
A practical example that can be used for other projects.

## Slide 3: Start with a sketch
Sketch on paper how your box looks like and the approximate dimensions.

## Slide 4: Define the parameters

## Slide 5: Create the front face
Make a new component
Sketch the face
  Add the tabs
  tabLength = length/(ntabs_1*2-1)
Extrude

## Slide 6: Add the side component
New component
Create sketch
  Start for ORIGIN
  Choose EDGE face of front tab
  Constrain sketch to the front component
  Draw the tabs
Extrude

## Slide 7: Mirror front to form back
Create a mid-plane
  Switch off visibility of front body to help
  Choose front and rear edges of side
Mirror the front using the mid-plane
Repeat for left and right sides

## Slide 8: Create the base
Rotate the object to bottom view
Create new component
  Create sketch
  Start from ORIGIN
  Sketch the base
  Constraint to edges
  Extrude

## Slide 9: Combine
Use the combine tool to create the tabs.
Turn OFF components that are not used to improve visibility

## Slide 10: Completed Model
Change your parameters, the box should change without problems
Some parameters do not work that well (which ones, why?)

## Slide 11: Check Model
Export and check the DXF of each of the components. Align them for laser cutting
Q: Does the thickness of the material affect the DXF output for laser cutting?

## Slide 12: Assignment: Musical Box
You are to create a closed box with a movable lid, specifications are as follows:
  Must have a movable lid
  Must be lasercut (wood 2.5~3.6mm)
  Must be able to accommodate “mechanical hand-cranked music box movement”
  Drawn and modelled in Fusion 360
  Can be glued together (no nails, hinges etc)
  Must be “decorated” in some manner

## Slide 13: Example: Music Box
Search: Musical Box Mechanical Hand Crank

## Slide 14: DIY Music Box
Hand Crank Musical Mechanism Craft DIY Music Box
Must accommodate musical hand crank
Measurements are approximate
You can omit the hole for the crank until the box is assembled.

## Slide 15: Marking Scheme
Item | Description | Score
1 | Fusion 360 Box design (.f3d included) – 25% Lid – 25% | 50%
2 | Laser cut box fitting | 20%
3 | Write-up (how-to) | 20%
4 | Fitting, Enhancements | 10%
Deadline for submission: Friday, Week 2 Term 2 (tentative)

## Slide 16: EP1000
Computer Controlled Cutting
End