## Slide 1: EP1000
Computer Controlled Cutting 2 Assignment

## Slide 2: Lasercut Parametric Box
Boxes are useful in all projects as they provide housing or containment.
Making the box parametric allows changes, accommodating for boxes of different sizes, types.
A practical example that can be used for other projects.

## Slide 3: Start with a sketch
Sketch on paper how your box looks like and the approximate dimensions.

## Slide 4: Define the parameters

## Slide 5: Basic Calculations
Odd number of tabs
Tabs and spacers have same size
Do NOT use the sketch > rectangular pattern to duplicate.
You CAN use the 3D create > pattern to duplicate the feature.

## Slide 6: Create the front face
Make a new component
Sketch the face
  Add the tabs
  tabLength = length/(ntabs_1*2-1)
Extrude

## Slide 7: Add the side component
New component
Create sketch
  Start for ORIGIN
  Choose EDGE face of front tab
  Constrain sketch to the front component
  Draw the tabs
Extrude

## Slide 8: Mirror front to form back
Create a mid-plane
  Switch off visibility of front body to help
  Choose front and rear edges of side
Mirror the front using the mid-plane
Repeat for left and right sides

## Slide 9: Create the base
Rotate the object to bottom view
Create new component
  Create sketch
  Start from ORIGIN
  Sketch the base
  Constraint to edges
  Extrude

## Slide 10: Combine
Use the combine tool to create the tabs.
Turn OFF components that are not used to improve visibility

## Slide 11: Completed Model
Change your parameters, the box should change without problems
Some parameters do not work that well (which ones, why?)

## Slide 12: Check Model
Export and check the DXF of each of the components. Align them for laser cutting
Q: Does the thickness of the material affect the DXF output for laser cutting?

## Slide 13: Assignment: Musical Box
You are to create a closed box with a movable lid, specifications are as follows:
  Must have a movable lid
  Must be lasercut (wood 2.5~3.6mm)
  Must be able to accommodate “mechanical hand-cranked music box movement”
  Drawn and modelled in Fusion 360
  Can be glued together (no nails, hinges etc)
  Must be “decorated” in some manner

## Slide 14: Example: Music Box
Search: Musical Box Mechanical Hand Crank

## Slide 15: DIY Music Box
Hand Crank Musical Mechanism Craft DIY Music Box
Must accommodate musical hand crank
Measurements are approximate
You can omit the hole for the crank until the box is assembled.

## Slide 16: Marking Scheme
Item | Description | Score
1 | Fusion 360 Box design (.f3d included) – 25% Lid – 25% | 50%
2 | Laser cut box fitting | 20%
3 | Write-up (how-to) | 20%
4 | Fitting, Enhancements | 10%
Deadline for submission: Friday, Week 2 Term 2 (tentative)

## Slide 17: EP1000
Computer Controlled Cutting
End

## Slide 18: Parametric drawings…
Some parametric drawings do not work.
The parametric changes made to the sketch (2D profile) do not carry over to the 3D model
Functions not recommended with parameters:
  Sketch: rectangular/circular patterns
  Sketch: mirror
  Hard coded profiles
Alternative: use 3D patterns with Features instead

## Slide 19: Sketch: Rectangular Patterns 1
Sketch is made using rectangular pattern with parameters

## Slide 20: Sketch: Rectangular Patterns 2
Pattern with parameters does not exist in 3D space as extrude is done on profile

## Slide 21: Sketch: Rectangular Patterns 3
Parametric change has no effect on 3D design

## Slide 22: 3D Parametric Features 1
Effect the feature (extrude) in 3D space

## Slide 23: 3D Parametric Features 2
Effect the feature (extrude) in 3D space

## Slide 24: 3D Parametric Features 3
Pattern the feature

## Slide 25: Results
Parametric design can still be applied in 3D space

## Slide 26: Parametric design in 2 axes
Need consideration on values to use as parameters
Perform some quick calculations and use them as the parameters
Select the proper axes/direction in which to apply

## Slide 27: Results 2 axes