## Slide 1
Notes: Videos to open
Cardboard Prototyping - https://youtu.be/k_9Q-KDSb9o
Cardboard Construction Techniques - https://youtu.be/MpjyOjPj98I
Rian Touag - https://youtu.be/g6xG-5YtesU

## Slide 2: Product Development & Prototyping
Rodney Dorville
Fablab Singapore Polytechnic

## Slide 3: CDIO Process
Notes: In any process development, you should always consider the CDIO process.
Conceive the idea, method, technology, pathway
Design your product, putting in constraints etc
Implement and make it
Operate and make changes improving the system
For new ideas – usually you don’t have the Time, Resources or Knowledge for a full blown development process
Hence, you prototype

## Slide 4: Prototyping
A prototype is an early sample, model, or release of a product built to test a concept or process
A chance to validate whether your idea matches users’ thoughts.
Fail faster, Succeed sooner
David Kelley
Ref: Wikipedia
Ref: Stanford Social Innovation Review
Notes: Use the CDIO process to create a prototype
It is a working model of how the actual product is going to look, feel and operate.
Leave the aesthetics and niceties to the final outcomes/designer
Let’s make it work!
The faster you fail, the sooner you recover, and get better results
David Kelly – Founder of IDEO (https://ssir.org/articles/entry/fail_faster_succeed_sooner)

## Slide 5: Pros & Cons
Advantages
Get a quick view (overview)
Can try different ideas
Find mistakes early
Switch tracks easily
Develop into a more refined product
Disadvantages
Time – needs proper planning
Cost
Resource intensive
Heartache

## Slide 6: Prototyping
Quirky: How to make a cardboard prototype (2 min)
Notes: Quirky shows how to go from an idea to a prototype using cardboard, he also shows the different techniques used in cardboard prototyping

## Slide 7: Paper prototyping
The simplest method.
Easy, quick, cheap, available everywhere, recyclable.
Great for a first effort.
However,
  Not robust
  Limited shapes for easy creation

## Slide 8: Print & Cut
The Punnet – card case for RPI
Some designs are available on the Internet
Complex designs may need skills and planning
Consider origami methods

## Slide 9: Cardboard Prototyping
Simple & easy mock-ups
100% recyclable
Can be done with a knife and ruler
Digital design
  2D drawing or 3D CAD design
  Flatbed cutter
Re-sizeable

## Slide 10: Corrugated Cardboard
Easy to manipulate
Sturdy
Easy to obtain
Recyclable
  Almost free
  Cheap

## Slide 11: Tools Required
Cutting Mat
Box Cutter
Metal rulers
Sturdy shears / scissors
Hot Glue Gun & glue sticks
Markers, pens, pencils
Masking tape
Machinist square 90o
Circular cutters
Adafruit: Cutting Tools and Techniques

## Slide 12: Techniques - Fasteners
Fixtures
  Masking Tape
  Double-side Tape
  White/Paper glue, UHU
  Hot-melt glue
Movement
  Cable Ties
Joints
  Split-pin tacks
  Rivets
Notes: Fixtures – depends on how fast you can work, and how fast the fixture is made
Masking tape – take your time, immediate fixture
Double sided tape – take your time, immediate fixture
White Glue – 30~60 minutes, 4 hours to set, 24 hrs full strength
UHU – 5~10 minutes, 1 hour to set, 4 hours full strength
Hot melt glue – 1 minute, 3~5 minutes to set, 10 minutes full strength
Cable ties are a fast way of joining items with a liberal degree of movement
Split-pin tacks allow 360 degree movement in the fixation plane
Rivets provide are stronger fix, with varying stiffness to the motion

## Slide 13: Techniques
Ref: Bay Area Educators Night
Notes: Bay Area has lots of nice ideas and samples

## Slide 14: Construction Techniques
Arianne Schnalzer – Cardboard Construction (6 min)

## Slide 15: Cardboard Prototypes
Kiosks
UV Sanitizer
Manu Prakash: Frugal Foldscope

## Slide 16: Blue Foam
XPS (Extruded PolyStyrene) foam
Available in blocks or sheets
Good for
  Solid modelling
  Authentic look and feel
  Large models and prototypes
Handling
  Manual techniques
  Digital Fabrication Machining

## Slide 17: Cutting Blue Foam – Hot Wire
Handheld foam cutters
Table top foam cutters

## Slide 18: Cutting Foam Shapes
AlfonsoTheTraitor: Cutting circles with a hot wire foam cutter
Quassi’s Bell Tower: How to Make a Circle Jig for your Proxxon Thermcut

## Slide 19: Foam Prototypes
Shaping Tools:
Carving knife
Hot Wire
Sandpaper
Rasp & Assorted Files
Heat Gun
Rian Touag: Foam Modelling - How To Make Rapid Prototypes (2 min)
Notes: Lots of tutorials and videos in the guides column

## Slide 20: Blue Foam Prototypes
Radio
Hot Glue Gun
Mouse
Foam prototypes add a SOLID touch/feel
Design Sojourn: Re-thinking the hair dryer
Notes: Blue foam allows a level of solidness.
If coated with a resin/paint/textured can be made to feel like the real product
Good for testing feels and ergonomics: Hair dryer grips: https://s3files.core77.com/blog/images/571176_34481_60264_gbSeIsTzL.jpg
Design Sojourn : Re-thinking the hair dryer (https://designsojourn.com/rethinking-the-hairdryer/)
Ariane Prin : Hair dryer concepts (https://s3files.core77.com/blog/images/571176_34481_60264_gbSeIsTzL.jpg)

## Slide 21: Guides:
Cardboard
  Adafruit: Cardboard Fundamentals - John Park
    Remember to also check out the links at the end of the article
  Making Society: Cardbord Shaping Techniques
Foam
  Juan Noguera - Blue Foam - Basic Model Making Techniques
  Icarus Games - An Introduction to Working With Blue Foam (Styrofoam)XPS
  Make: Skill Builder: Styrofoam Sculpting, Surfacing, and Sugru Skinning
  CARVING FOAM: How To Carve Polystyrene Projects

## Slide 22: Product Development & Prototyping
Rodney Dorville
Fablab Singapore Polytechnic