## Slide 1: EP1000
3D Models - 2

## Slide 2: Methods of Creating 3D Models
Extrusion
  Use a 2D plane profile
  Extend into the 3rd plane
Rotation
  Use a 2D plane profile
  Rotate the plane around an axis
Sculpting
  Start with a 3D object
  Add, remove 3D objects
  Subdivide the surface into sections
  Push, pull, extend, contract sections

## Slide 3: Create > Revolve
Start with a 2D closed profile in plane
Create > Revolution
  Select the axis of revolution
  Select the angle to revolve

## Slide 4: Create > Revolve
Revolve used for
  Uniform objects revolved about an axis
  Creates objects not possible with Extrude
What profiles were used to create these objects?

## Slide 5: Revolve using Arc profiles
You can create bottle objects using arc profiles.
You can also use the revolve command to cut parts which you do not need.

## Slide 6: Exercise 1: Mug with Handle
Let's make a mug with a handle
  dimensions: 50mm (diameter), 80mm (height)
  Include an arc at the base of the mug
  let the mug’s thickness be about 2.5mm
  add a handle (ear) of thickness 6mm of your choice
Go wild with your design! It’s just an exercise on using the revolve and extrude functions.

## Slide 7: Tip 1:
You can use the profile as a guide.
Make sure you have a closed profile before you revolve.
Also, ensure that you do NOT overlap across the axis

## Slide 8: Tip 2:
Create the handle on the mid-plane.
Project the mug onto the plane to get the intersect points.

## Slide 9: Exercise 2: How to model a Hex Nut
This is Kevin Kennedy’s video tutorial on the modelling of a hex nut: https://youtu.be/Xho87HJ-XDo
A useful tutorial should you need to create odd-sized fasteners.

## Slide 10: Exercise 3: Chess piece - Knight
Design a Knight chess piece:
  Base: 30mm
  Height: 50mm
  Head thickness: 5mm
Use a template for the head
The base should be hollow

## Slide 11: Tip: Use a canvas
Let’s cheat and use a template (do a Google search)
  Insert > Canvas
  Adjust transparency
  Adjust position
  Create Sketch
  Draw the profile
  Switch off canvas

## Slide 12: When you have finished…
Embed your Fusion 360 file in your web page
Ref:
  Fusion 360 How to embed a viewer of a Fusion 360 design into a website
  EP1000 Assignment: 3D Modelling
Include this exercise in your documentation, including the steps taken

## Slide 13: Sculpting
Use a basic 3D shape, break up the shape, manipulate each part.
Like playing with plasticine

## Slide 14: Sculpting
Product Design Online Tutorials:
  How to sculpt an Earbud
  Sculpting for plastics parts: Part 1, Part 2
Good for creating objects with no definite shapes
Time consuming
Great Effects

## Slide 15: EP1000
3D Models - 2
End