## Slide 1: EP1000
Embedded Systems 1

## Slide 2: Embedded Systems
A dedicated computer system with a dedicated function within a larger system to perform a specific task. E.g. smart TVs, ovens
After development with a microcontroller, the circuit could be reduced to a single IC with support devices.
AudioQuest Dragonfly audio Digital-Analog Converter

## Slide 3: Microcontroller Systems
Combines
  Microcontroller
  Memory (RAM, ROM)
  Input Output
    Digital
    Analog
    Interface protocols
  Timing
  Other peripherals
Into a Single chip

## Slide 4: Common Microcontrollers
Atmel
  ATTiny 45, 44, 412, 1614
  ATMega 328, 3u24
ARM
  D11C, D21E
Xtensa
  ESP8266, ESP32
  Integrated RF, Bluetooth, networking

## Slide 5: The Arduino Embedded System
An Arduino Embedded System comprises of
  Software & Software Tools
    Integrated Development system (IDE)
    Arduino programming language (based on Processing)
    Development & Debugging Tools
    Software libraries
  Hardware
    ATmel processor boards (and others)
    Shields (add-on modules)
    Sensors, actuators, peripherals
  Open Source Platform

## Slide 6: Arduino Systems
A hardware and software company based in Italy
Initial development – software (based on Processing) and later hardware boards (Atmel based)
Produces and markets “official” boards: Uno, Due, Leonardo, Diecimila, Mega, Nano
Software and hardware is open source.

## Slide 7: Why use Arduino Systems
Open source libraries & support
Inexpensive, lots of clones, 3rd party manufacturers
Simple, clear programming environment using GUI
Cross-platform (Windows, MacOSx, Linux)

## Slide 8: Arduino Uno
Most common microcontroller board to begin Arduino projects.
Uses a ATmel Atmega328P processor with a separate programmable interface using another Atmel processor and USB.
Has sockets for interfacing and power.
So popular that it is called Arduino. (Please don’t make this mistake!)
“Arduino” or “Uno”

## Slide 9: Variations of the Uno
Being open-source, there are many variations.
Programming and usage are basically the same with some minor variations.
All boards use the ATMega328P processor (may be in different formats)
All boards have the same I/O pins
Difference is in $$cost$$

## Slide 10: Main Uno board difference
Expensive boards use the FTDI chip for USB China clones use the CH340 chip
Need to install the CH340 drivers.
Lots of tutorials from Google

## Slide 11: Uno Board Features

## Slide 12: Uno Board Features
Power
  Can be powered from USB port (<0.5A)
  External power from DC jack 6V ~ 12V
  Power outputs: 0 (GND), 3.3V, 5.0V (up to 0.3A), Vref (5V)
Digital Input/Output pins
  Can be configured as Input, Output or Pull-Up Inputs
  Has Pulse-Width-Modulation on ~ indicated Pins
  Built-in LED on Pin13
Analog Inputs
  10-bit Analog inputs
Others
  Serial I/O interface
  I2C interface
  SPI interface

## Slide 13: Programming the Uno
Requires an Integrated Development Environment
  Download from Arduino.CC
  Suggest using v2.0 BETA because of features
Arduino programs are called sketches.
  In text
  Have extension .ino

## Slide 14: Programming: Getting Started
Saved as sketches (extension .ino)
Follows most characteristics of a C++ syntax/structure
Always has 2 functions:
    setup() – code is only executed once
    loop() – code is continuously looped

## Slide 15: setup()
Executed only ONCE after each powerup or reset of the UNO.
UNO is automatically reset after each successful sketch upload
Contains
  initialization code
  initialization of variables
  setup and configuration of I/O ports
  setup of other interfaces
Tip: Use identifiers to name your I/O pins, it makes programming and code recognitions much easier

## Slide 16: loop()
The loop() function is executed after the setup() code completes.
Loops infinitely executing code within the loop() function.
Place your code/program within this function, there is NO stopping this code

## Slide 17: Coding Tips
Arduino code is loosely based on C++ (actually Processing)
Follow good C++ programming habits:
  use comments
  indent your code
  use UPPERCASE to denote constants or defines
  name your variables intelligently

## Slide 18: Digital Input/Output
ATMega328 has 14 digital I/O Pins
  labelled pin0 to pin13
  Pin0(Tx), Pin1(Rx) are assigned as Serial I/O
  Pin3, Pin5, Pin6, Pin9, Pin10 and Pin11 have PWM functionality
Digital values
  0 (0 V, GND, ON, LOW)
  1 (5 V, Vcc, OFF, HIGH - typically > 3.3 V)
Some pins are multifunctional, i.e. have different functions depending on how they are initialized.
  inputs (default)
  inputs with pull-up resistors
  outputs
  Pulse Width Modulation outputs

## Slide 19: Digital Input/Output
Arduino provides useful library functions simplifying these operations
  pinmode() - initialises the pin
  digitalRead() - reads/inputs a digital value
  digitalWrite() - outputs a digital value
  analogWrite() - outputs a PWM

## Slide 20: Digital Output
Let's blink (turn ON/OFF) the on-board LED
  pinMode() initialises pin13 to be an OUTPUT pin
  digitalWrite() outputs a 0 or a 1 alternately
  delay of 1 second to allow us to view the result

## Slide 21: pinMode( pin, MODE )
Configures specified pin to behave either as input or output.
Modes available
  INPUT digital input mode (high-impedance states)
  INPUT_PULLUP digital input mode with internal 20K-50K ohm pull-up resistor
  OUTPUT digital output mode able to source up to 40mA per pin, total of 200mA per chip

## Slide 22: Using an External LED
Let’s blink an external LED
  need to WIRE-up the circuit
  requires a current-limiting resistor
  change the pin to 8
  Compile, Upload, Execute!
What is the purpose of the resistor? Which pins can be used as output pins?
Can you add additional leds?

## Slide 23: Assignment: A countdown timer
Seven segment LED
  Made up of 7 separate LEDs
  Combined in segments, forms digits
Change the switches to see the effect
TinkerCAD: CC 7 Seg LED

## Slide 24: Assignment: A countdown timer
Experiment with the 7-segment circuit
Convert the circuit which uses an Uno to control the 7-segment CC display
Write a program that counts from 0 to 9 continuously
Why I should use Arduino IDE 2.0?
Why can’t I use a single resistor at the CC pin?

## Slide 25: EP1000
Embedded Systems 1
End