## Slide 1: EP1000
Digital I/O

## Slide 2: Digital I/O
The Uno uses the ATMega328 processor, which has 14 digital I/O pins (Some of these pins are multifunctional)
A digital I/O pin can input or output digital (0, 5V) signals.

## Slide 3: Digital I/O functions
The Arduino system provides 3 functions for the manipulation of digital I/O.
You need to
  Configure the pin (pinMode()), before
  Using the pin
    digitalWrite() output
    digitalRead() input
Digital I/O functions
digitalRead()
digitalWrite()
pinMode()

## Slide 4: pinMode(pin, MODE)
Configures specified pin to behave either as in input or an output.
Modes available:
  INPUT digital input mode (high-impedance state)
  INPUT_PULLUP digital input mode with internal 20K~50K ohm pull-up resistor
  OUTPUT digital output mode able to source up to 40mA per pin, total of 200mA per chip

## Slide 5: digitalWrite(pin, {LOW|HIGH})
Outputs a LOW (0V) or HIGH (5V) to a digital pin.
The digital pin must be configured as OUTPUT.
You can also output a LOW to create a GND for sinking current!

## Slide 6: Driving an LED
An LED lights up (conducts) if a correct voltage is applied to the pins.
When the LED conducts, current is allowed to pass through. The LED drops about 2V.
We need to limit this current (10~20mA) otherwise, we will get a short-circuit.
Current limiting resistor value: R = V / I = (5 – 2V) / 10 mA = 300 ohms
LED current depends on type, check data sheet for forward voltage and current limits. Watch: GreatScott! Everything about LEDs

## Slide 7: Digital Input
We can use digital inputs to read the status of the switches in a circuit.
Need to add a current-limiting resistor to prevent short circuits.
Usual value is 10 kOhm
States:
  A - normal HIGH, when closed LOW
  B – normal LOW, when closed HIGH
Circuits by CircuitLab

## Slide 8: Digital Input
How to use PB switches with digitalRead()

## Slide 9: Internal Input Pullup Resistor
We can use the internal pullup resistor by changing the mode
pinMode(pin, INPUT_PULLUP)
Internal pullup resistor is 20K~50K which limits the current.
Uno input pullup resistor demo

## Slide 10: Problems with Mechanical Switches
When a mechanical switch is pressed, it creates transients (bouncing) which causes incorrect states to be read.
Solution:
  Software debounce
  Add a delay
  Use states
Software Debounce of buttons

## Slide 11: Counting with a Switch
PBSW uses internal pullup resistor.
Each time the switch is pressed, the count is incremented. The LEDs should show the binary equivalent of the count
Sequence: --, -R, G-, GR repeats
Simulate and examine result, does it work as stipulated?
Counting With a Switch

## Slide 12: Code: Counting with a switch
How do we debug this code?

## Slide 13: Arduino Serial Mode
The Arduino System provides a Serial Mode for displaying text messages.
Uses the Uno’s serial port to transmit data to and from the board to the IDE
Allows data to be displayed in text as well as in graphical format.
Uses the Arduino Built-in library: Serial
When using Serial, you must not use the Tx,Rx pins for any I/O.

## Slide 14: Serial Library
Use Serial to display the count value from a sketch. The sketch updates the count value and flashes an LED with a delay of 1 second between flashes.
Serial.begin(9600) Sets the data rate in bits/sec for serial data transmission
Serial.print(data) Serial.println(data) Sends data to the serial port for conversion and output. If a string of text is sent, it must be delimited with double quotes (“)
There are other functions, but usually not used in embedded circuits.

## Slide 15: Where does the serial output go?
There is an icon/text “Serial Monitor” on both the TinkerCAD and Arduino IDE interface to show the contents of the serial monitor.
You can clear, input and output data as well as graphically chart the data you receive from the embedded system.
Using the Serial Monitor

## Slide 16: Debug our Counting SW program
Looks like we have bouncing problem and/or the switch is being read too fast (SW not recovered yet)
Debugging the SW counting program

## Slide 17: Pushbutton SW
We keep reading the PBSW taking note of the digital values
We maintain the state so that we know which part of the sequence we are currently in and when the PBSW returns to normal
Register the entire sequence as a single push.
threshold
HIGH
LOW
1 push count
HIGH
LOW
HIGH
STATE
Record SW event

## Slide 18: Using states
Use states to track the keypress.
HIGH = normal LOW = in a keypress HIGH = returns to normal
Add short delay when key is pressed to remove bouncing
Record the keypress only when the sequence is complete.
Reading a Pushbutton using states

## Slide 19: Assignment: Programming
Work out Assignment 12 Introduction to Arduino Programming using TinkerCAD.
Simulate your solution using TinkerCAD. Use Serial to display messages showing the states and to show that you know how to use the library and the serial monitor.
Document your work on your site.

## Slide 20: EP1000
Digital I/O
End