## Slide 1: EP1000
Embedded Systems 2 Programming

## Slide 2: Arduino System
Programs written for the Arduino system are text files called sketches (extension .ino)
The programming language used is based on Processing, which is loosely based on the C++ syntax.
A simple and easy introduction to Programming Arduino. Available in the SP Library

## Slide 3: Sketches
All Arduino sketches have 2 functions:
  setup() code is executed only once used for initialisation and setup of I/O
  loop() code is executed continuously application code is placed here

## Slide 4: Variables
Variables are memory set aside to hold changing data.
Variables use different amounts of memory depending on the data type used.
Common data types are
  char 8-bit
  int 16-bit
  float 32-bit
  String stores a sequence of characters
We use identifiers (names) to name the variable and locate it.
Use conversion functions to convert between them
Data Types
array
bool
boolean
byte
char
double
float
int
long
short
size_t
string
String()
unsigned char
unsigned int
unsigned long
void
word

## Slide 5: Operators
Arithmetic Operators
% (remainder)
* (multiplication)
+ (addition)
- (subtraction)
/ (division)
= (assignment operator)
Boolean Operators
! (logical not)
&& (logical and)
|| (logical or)
Compound Operators
%= (compound remainder)
&= (compound bitwise and)
*= (compound multiplication)
++ (increment)
+= (compound addition)
-- (decrement)
-= (compound subtraction)
/= (compound division)
^= (compound bitwise xor)
|= (compound bitwise or)
Bitwise Operators
& (bitwise and)
<< (bitshift left)
>> (bitshift right)
^ (bitwise xor)
| (bitwise or)
~ (bitwise not)
Use the KISS principle!
Operators work only with similar data types
Use conversion functions to help.

## Slide 6: Boolean
Boolean variables have only 2 values: True/False
Boolean expressions have only 2 results: True/False
Comparison operators give a Boolean result
Boolean operators work only with Booleans
Comparison Operators
!= (not equal to)
< (less than)
<= (less than or equal to)
== (equal to)
> (greater than)
>= (greater than or equal to)
Boolean Operators
! (logical not)
&& (logical and)
|| (logical or)
Used in Conditionals, Loops

## Slide 7: Conditional: if … else
Control Structure which checks the condition expression and if true executes the following code block.
Condition Expression is a Boolean expression.
When used with the else, control transfers to the else block.
Can have nested or have multiples else-if conditionals for more granular control.

## Slide 8: Conditional: switch … case
Control Structure which checks the value in switch (preferably ordinal) and transfers control to the matching case code block.
Each case code block must be terminated with a break.
Each case must match exactly.
Control is transferred to the default code block (if any) if there is no match.

## Slide 9: Loop: for
Structure of for
  Initialization
  Conditional expression
  Increment
Used when we know exactly the number of times we wish to loop.
Loops a fixed number of times

## Slide 10: Loop: while
Tests conditional expression, if true the code block is executed.
Indefinte loop, code block is executed zero, once or many times.
If the condition results always in True, we have an endless loop.
Loops a 0, 1 … n number of times

## Slide 11: Loop: do … while
Executes the code block before testing the conditional expression.
If conditional expression is true the code block is repeated.
Indefinte loop, code block is executed once or many times.
If the condition results always in True, we have an endless loop.
Loops a 1 … n number of times

## Slide 12: Control: break
When used in a loop, break exits the loop, control transfers to next statement after loop.
break is also used to transfer control out of a matching case in a switch statement.
Control: continue ignores the remaining statements and transfers control to the loop condition. (not commonly used)

## Slide 13: Functions
A function is identified using ()
A function is a block of code that can accept parameters.
Executes the code when called, returns a single value as it’s name.
return is used to return the value in the indicated data type.

## Slide 14: Class
A user-defined data type that is used to create objects.
An object has
  attributes (constants, variables)
  methods (functions)
An object’s attributes and methods are accessed using the dot (.) operator
Classes are predominantly used in code libraries
Classes should be identified using a starting uppercase character e.g. Serial

## Slide 15: Directive: #define
#define is a compiler directive and not a code statement.
Does not end with a semi-colon
Used to name a constant and assign the value
const is the preferred method of defining constants
Constants should be identified using uppercase

## Slide 16: Directive: #include
#include is a compiler directive and not a code statement.
Does not end with a semi-colon
Instructs the compiler to read and insert code from the target file
< file > indicates system library, found along the library path
“ file “ indicates local file in same folder

## Slide 17: EP1000
Embedded Systems 2 Programming
End